## Slide 1: Comparison and Error Modeling of Velocity-Based Initial Orbit Determination Algorithms
Linyi “Tiger” Hou, Kevin Lohan, and Zachary R. Putnam
University of Illinois at Urbana-Champaign

## Slide 2: Introduction
Velocity-based initial orbit determination (VIOD)
  Uses only velocity vectors
  Does not depend on the Deep Space Network
  Little error analysis has been previously performed
  No error models have been previously developed
v1
r1
r2
r3
v2
v3
ϕ3
ϕ2
ϕ1
t1
t2
Gibbs’ Method
Laplace’s Method
Lambert’s Method
Velocity IOD
r1
r2
r3
Gibbs’ Method
ϕ3
ϕ2
ϕ1
t1
t2
Laplace’s Method
t1
Lambert’s Method
r1
r2
v1
v2
v3
Velocity IOD

## Slide 3: Outline
Overview of VIOD Algorithms (with proposed improvement)
Comparison of VIOD algorithms
Error Modeling for Hodograph-based VIOD
Validation of Error Model
Example: Predicting VIOD Error

## Slide 4: The Orbit Hodograph
v2
v1
Central Body
Δf
O
v3
Δf
R
c
v1
v2
v3

## Slide 5: The Hodograph Method
Perform circle fit on velocity vectors to find hodograph
  Find the orbit plane using singular value decomposition (SVD)
  Project velocity vectors onto orbit plane
  Perform 2D circle fit on projected velocity vectors
Retrieve position vectors from hodograph

## Slide 6: The Improved Method
Same process as HM, but different circle fitting algorithm
  Hyper-accurate circle fit (“Hyperfit”) by A. Al-Sharadqah and N. Chernov
Reduces fitting error when arc span is small relative to noise

## Slide 7: Simulation and Error Evaluation
Simulate two-body motion, measure velocities over 10% of orbit
  Obtain 20 velocity vectors and corresponding positions
Apply independent sensor noise to each measurement
  Obtain perturbed velocities
Perform VIOD using 3000-sample Monte Carlo simulations
Calculate relative root-mean-square error of the first position

## Slide 8: Accuracy
Improved Method > Hodograph Method > Energy Method

## Slide 9: Computation Speed
Improved Method = Hodograph Method > Energy Method

## Slide 10: Modeling VIOD Error using the Hodograph
Is hodograph fitting error () a good predictor of VIOD error ()?
Expect to change in the same way as when conditions varied
Case 2
Ratio
Case 1
Case 3
Constant

## Slide 11: Modeling VIOD Error using the Hodograph
Is hodograph fitting error () a good predictor of VIOD error ()?

## Slide 12: Error Models
Find using Kepler’s equation,

## Slide 13: Validation: Eccentricity
# of Measurements | 10
Tot. Measurement Time | 10% orbit period
# of Measurements | 10
Tot. Measurement Time | 10% orbit period

## Slide 14: Validation: Initial True Anomaly
# of Measurements | 10
Tot. Measurement Time | 10% orbit period
# of Measurements | 10
Tot. Measurement Time | 10% orbit period

## Slide 15: Example: Predicting VIOD Error
Calculate VIOD error of any orbit using Monte Carlo simulations
Use analytic error model to convert to desired orbit
* Denotes reference orbit

## Slide 16: Example: Predicting VIOD Error Cont’d
Reference Orbit (RMSE=7.23%):
  ,
  ,
  ,
Target Orbit:
  ,
  ,
  ,
Predicted Error: 15.39%
Monte Carlo Error: 15.01%

## Slide 17: Conclusions and Future Work
Improved hodograph-based VIOD algorithm
Developed & validated error model for hodograph-based VIOD
---
Accommodate changes in other parameters
  e.g., the measurement duration and the number of measurements
Eliminate need for the error of a reference orbit
Generate error bounds from VIOD results

## Slide 18: Thank you!